## Slide 1
Weight and Balance

## Slide 2: OBJECTIVES
Determine the “flying” weight & balance
Determine your ‘pilot moment arm’ and the aircraft empty weight (optional).
(Requires a second weighing)
Ballast the aircraft to desired CG.

## Slide 3: REQUIRED EQUIPMENT
Suitable scales (For main and tail wheel)
Level, Plumb Bob, and Tape Measure
Suitable blocking to support ‘tail’ scales with the aircraft ‘leveled’.
Enclosed Area
Two People (minimum)

## Slide 4: REQUIRED INFORMATION (From W&B or Manual)
Datum Plane Location - Usually the wing leading edge at the wing root.
‘Leveling’ criteria – Usually a level placed on the fuselage ahead of the fin with a defined taper (ratio) between the fuselage and level.
Distance (usually “A”) from datum to the main wheel.
Distance from datum to the tail wheel or skid.
(usually “A” plus “B”)

## Slide 5: SAILPLANE PREPARATION
Position the level, with appropriate blocking / offset taped in place.
Chock the main wheel on the scales.
Install the batteries, drinking water, and whatever else gets added for flight such as the pilot and parachute.
Raise tail and position scales, with appropriate support, in correct attitude, per level bubble.
Note: Tail lighter with pilot in cockpit.

## Slide 6: TAKING THE DATA
Checks- Canopy closed, wings balanced (no wing stands), level removed, no other points of contact.
Record scales readings (main and tail
Record tare (wheel chock etc.)

## Slide 7: CALCULATIONS (Aircraft, flying config.)
Item Weight Station Moment
M. Wheel 841 lbs 7.00 inches 5887 in.-lbs
T. Wheel 28.5 178.31 5081.8
A/C, Flying 869.5 12.62* 10968.8
* Station = moment / weight =1096.8 / 869.5 = 12.62

## Slide 8: CALCULCATIONS (BALLAST WEIGHT)
ITEM WEIGHT STA. MOMENT
Aircraft 869.5 12.62 10968.8
Ballast 25 175.0 4375.0
A/C & bal 894.5 16.85 15073.8