## Slide 1: Outlandings
f
std

## Slide 2: Planning
Always calculate glide ratio to a landable area
The fields might be short
You need som height for planning a good circuit
Keep your mobile phone turned on, it can be traced by the SAR

## Slide 3
In every gliding hand book!
The agreed standard!

## Slide 4
Competition traces
Accepted substandard??

## Slide 5
Own decision?
If they go then I go

## Slide 6
Own decision?
If they go then I go

## Slide 7
Own decision?
If they go then I go

## Slide 8
Own decision?
If they go then I go

## Slide 9: Up hill landing

## Slide 10: Water landing
Is not a normal option
Can be dangerous
But, probably safer than to the forest or a clearing in the forest
The clearings may look green and nice from the air, but are NOT nice on the ground

## Slide 11: Experience
About 10 water landnings in Sweden the last 15 years
No serious injuries or damages
The glider have flown the next day in many cases

## Slide 12: Before landing
Call on the radio
Turn of master switch
Prepare mentally
Locate the seat belt lock
Locate the canopy emergency jettisson

## Slide 13: Where to land?
Deep enough
Along the shore
Down wind side of the lake

## Slide 14
Wind
Wind

## Slide 15: How to land?
Gear down
Low speed, but main wheel first
Flaps in thermalling position
Airbrakes closed (if possible)

## Slide 16
Suction
Alfa increases
Stall

## Slide 17: After landing
You are not in a hurry
The glider floats
Open the canopy normally
Sit on top of the glider and think
Make a plan
Don’t swim with clothes on
Don’t try to swim with head wind

## Slide 18: Problems
The canopy might crack (sharp edges)
Swimming (with clothes)
The water is cold ( maybe < 10o C)
To get contact with the civilisation
Mobile phone is wet
pr