## Slide 1: Flying MacCready
What Do The Numbers Tell Us?

## Slide 8: Glider Wing Designed for 1 G MacCready flight takes glider out of optimum “bucket”
straight path
MacCready path
_ _
+ +
_ _

## Slide 9: Flight Path Is Longer For a 500’ pull up over 4000’ distance, add 125’
If 40 pull ups + 40 push overs
then flight is 10,000 ‘ longer
which = 2 minutes or 11 pts/day
<---- + 125 ft ---->
<---- + 4000 ft ---->
500 ft

## Slide 10: Inertial & Instrument Lag Conspire Against Theory
thermal
90mph
2 secs
(264 ft)
60 mph
6 secs
(570 ft)
reaction
sink
40 mph
reaction
2 secs
(116 ft)
Due to instrument lag, pilot is fooled into thinking s/he was in lift longer than s/he actually was.

## Slide 11: MacCready Flying Requires Attention That Could Otherwise Be Applied to: Navigation - Least sink route Lift detection - clouds, gaggles Avoiding mid-air collisions

## Slide 12: Speed vs Climb Rate

## Slide 13: Modified MacCready
Initiate pull up according to seat-of-the-pants
Use a diluted or averaged flight path
For known lift (clouds, gaggles, etc.), pull up prior to thermal so transit is slow
Fly inter-thermal speed according to: thermal strength, height of thermal, altitude of glider, outlook ahead.

## Slide 14: Thank you for attending!