## Slide 1
Final
Glides
US Team
Region 1 Comps
Doug Jacobs

## Slide 2
Final Glide – In Theory
Simple: Keep flying climb and glide on course
Leave the last thermal
When you can fly the McCready speed and
reach the goal
Plus a safety margin
Wind now a factor
Glide angle over the ground
Flatter with a tailwind
Steeper with a headwind
As is wing loading and bugs
Set your calculator accurately
Which requires practice
Why so important?
Not, for badge and distance flights
Very, for speed tasks and competition
Significant improvement to average speed

## Slide 3
Final Glide in Practice
Know your calculator:
Elevation - Terrain height
Arrival Height - Energy to Land Safely
Safety Margin - Extra Altitude
Common Errors
Climbing in weak lift – off McCready setting
Keep the thermal selection discipline
Going straight home – up a sink street!
Keep flying the energy lines down to arrival height
Taking too much
And steaming home at 130kts, doing 15:1
Taking too little
And trying to oomph up on the glideslope

## Slide 4
Psychological Pressures are intense on Final Glides
Glide angle visually flat in modern glass
“I’ll never make it”
Especially downwind
Excessive sink might be encountered
Flying very fast, very loud, very low
And the turbulence gets rougher lower
And the pilot’s IQ starts to fade
Tunnel visions/narrowed focus dangerous
Must fly the airplane to a safe landing, not just a good finish

## Slide 5: Final Glides in Contests
Final Glides around corners
Enough height for FG before last TP reached
Headwind/tailwind switchover at TP
“Steering” TP’s to direct finishing traffic
Final Glides in MAT’s, AAT’s
Want FG to be the largest proportion of overall flight possible
Why? – Because it’s your fastest leg
How? – come in just after Minimum Time
- we’ll discuss further in Contest Strategy

## Slide 7
Final Glide

## Slide 8
Hobbs 18M Nationals 2006
Long final glide adds
Significantly to avg speed

## Slide 9
You’ve got to practice, practice
Practice
To get a
Good Finish!