## Slide 1
Field Briefing

## Slide 2: 25 Air
Grid Area
Assembly

## Slide 3: Assembly
Grid Area

## Slide 4: 01 Air
Grid Area
Assembly

## Slide 5: 01 Ground
Grid Area
Assembly

## Slide 7
  Grid in areas discussed
  On weekend leave room for PGC Ops
  Grid time 11:30 +/- announced at pilot mtg.
  Grid groups together
  Remember gridding is a cooperative effort
Gridding

## Slide 8
  Launch time will be determined by the camp directors
  Launch in groups (classes)
  Once launch begins be ready to go
    Be belted in, checklist done …
    If you are not ready tell launch crew
Launch

## Slide 9
  Towpilot and ground operation will monitor 123.075
  L-19 is 05A, Pawnee is 76P be specific
  Tow pilots will follow track discussed
  Emergency straight ahead
    25 field left of school
    01 field of end of runway
Tow

## Slide 10: Tow
  Standard tow will be 2000’ AGL
    You may release early if you like
    Release under tension

## Slide 11
  Do not try to make a low save in the traffic area
  Announce your landing on 123.075
  Land according to traffic patterns
  Roll clear of the runways
    Others may be behind you
  Ground crew will tow you to the end of the launch line
Relights

## Slide 12
  Field elevation at PGC is 670
  Pattern altitude is 1500 MSL
  Runways 01 and 25 are left patterns
  Runways 07 and 19 are right patterns
  Announce landing on 123.075
  All runways are right rollout for gliders
Landing