## Slide 1: AIRCRAFT INSTRUMENTS
SPRING 2007 PERRY CROSS COUNTRY CAMP
PRESENTED BY
RICHARD KELLERMAN (QV)
TEAM USA
WHAT YOU SEE IS NOT WHAT YOU GET

## Slide 2: “STICK AND RUDDER”
AIRCRAFT DON’T BEHAVE THE WAY PILOT’S THINK THEY DO
NEITHER DO INSTRUMENTS

## Slide 3: WHAT THEY SAY AND WHAT THEY DO
WHAT IT SAYS IT MEASURES
ALTIMETER: HEIGHT
ASI: SPEED
COMPASS: DIRECTION
VARIO: RATE-OF-CLIMB
WHAT IT DOES MEASURE
STATIC PRESSURE
TOTAL – STATIC PRESSURE
LOCAL MAGNETIC VECTOR
GLIDER ENERGY

## Slide 4: THE PANEL

## Slide 5: THE ALTIMETER

## Slide 6: OVERVIEW
MEASURES STATIC PRESSURE
DISPLAYS ALTITUDE
USES STANDARD ATMOSPHERE
REQUIRES A REFERENCE
NUMEROUS ERRORS

## Slide 7: ERRORS
NONSTANDARD TEMPERATURES OF THE ATMOSPHERE
NONSTANDARD ATMOSPHERIC PRESSURE
AIRCRAFT STATIC PRESSURE SYSTEMS (POSITION ERROR)
INSTRUMENT ERRORS

## Slide 8: STANDARD ATMOSPHERE
HYPOTHETICAL VERTICAL DISTRIBUTION OF T, P, AND ρ
ASSUMED:
  TO BE A PERFECT GAS
  TO OBEY THE HYDROSTATIC EQUATION
  TO CONTAIN NO WATER VAPOR
  ACCELERATION DUE TO GRAVITY CONSTANT

## Slide 9: ALTITUDES
GEOMETRIC
  GPS
  RADAR
GEOPOTENTIAL
  PRESSURE
  DENSITY
Notes: http://mtp.jpl.nasa.gov/notes/altitude/altitude.html
http://mtp.jpl.nasa.gov/notes/altitude/AviationAltiudeScales.html

## Slide 10: ALTIMETER SETTINGS
FOR A PARKED GLIDER:
QNE: SET KOLLSMAN = 1013.2 hPa (29.92 IN)
  SHOWS PRESSURE ALTITUDE
QFE: SET KOLLSMAN = STATION PRESSURE
  SHOWS ZERO IN STANDARD ATMOSPHERE
QNH: SET KOLLSMAN = BAROMETRIC PRESSURE
  SHOWS FIELD ELEVATION IN STANDARD ATMOSPHERE

## Slide 11: THE SEA BREEZE
DID HE SAY SEA BREEZE?
YES – IF YOU UNDERSTAND THE SEA BREEZE YOU WILL UNDERSTAND PRESSURE LEVELS

## Slide 12: THE SEA BREEZE, WRONG!

## Slide 13: THE SEA BREEZE, RIGHT

## Slide 14: AIR ALOFT FLOWS OFFSHORE

## Slide 15: LOCAL HIGHS AND LOWS SET UP

## Slide 16: ALTIMETERS AND GLIDERS
TERRAIN CLEARANCE
200 FT!
QNH NOT QFE
CROSS COUNTRY HEALTH
RIDGES
FINAL GLIDE CALCULATIONS

## Slide 17: FINAL GLIDE CONSIDERATIONS
INSTRUMENT ERRORS CANCEL
PRESSURE CHANGES ONE INCH = 1,000 FT CAN BE +/- 200 FT
NON-STANDARD LAPSE RATE – DEVIATIONS GENERALLY POSITIVE 100 – 300 FT AT 5,000 FT AND 300 – 900 AT 15,000 FT.

## Slide 18: THE ASI

## Slide 19: WHAT IT MEASURES
Pstagnation = Pstatic + ρV2/2

## Slide 20: WHAT IT SHOWS

## Slide 21: WHY “INDICATED AIRSPEED”?
DEPENDS ON ρV2/2
AERODYNAMIC FORCES ALSO DEPEND ON ρV2/2
WHY QUADRATIC IN V?
IAS AND TAS FOR A 747 AT 40,000 FT?

## Slide 22: ASI’s AND GLIDERS
WESTERN FLYING
FINAL GLIDES
CROSS COUNTRY ENERGY MANAGEMENT

## Slide 23: THE CLOCK

## Slide 24: WHY A CLOCK?
FLYING TIME CONTROLLED TASKS
WRITE DOWN START TIME, THEN FINISH TIME
GETTING HOME
TIMELY REMINDER THAT WHEN THERMALLING VMG IS ~ ZERO
KNOW WHERE YOUR GPS CLOCK HIDES

## Slide 25: THE COMPASS

## Slide 26: BOXING THE COMPASS

## Slide 27: MODERN ROSE

## Slide 28: SWINGING THE COMPASS
FIND A ROSE
ORIENT N, NOTE READING
ORIENT S, ADJUST 50% OF ERROR
REPEAT TO CONSTANT ERROR
REPEAT FOR E/W

## Slide 29: USING THE COMPASS
GPS IS SIMPLY BETTER
USELESS EXCEPT IN UNACCELERATED FIGHT
VCC USEFUL FOR SITUATIONAL AWARENESS
LOCATING OTHER GLIDERS

## Slide 30: WHERE ARE YOU?
280
/20 SM
300
/15 SM
GOAL
YOU
YOUR BUDDY

## Slide 31: HERE I AM…
IF THE OTHER GLIDER HAS A BEARING TO A GOAL GREATER THAN YOURS HE’S ON YOUR LEFT
IF HE IS CLOSER HE’S AHEAD OF YOU
IF HE’S FURTHER, LOOK BEHIND
SAME BEARING, SAME DISTANCE – LOOK OUT!

## Slide 32: THE EYES HAVE IT

## Slide 33: LOOKING OUT
OTHER AIRCRAFT
CLOUDS
HAZE DOMES
TERRAIN FEATURES
BIRDS, OTHER GLIDERS, TRASH
ALL THE INSTRUMENTS

## Slide 34: GLIDESLOPE AND STF COMPUTER

## Slide 35: USE
ESSENTIAL FOR FINAL GLIDES
PRACTICE!
PRETTY MUCH ESSENTIAL WHEN RUNNING
CAN BE PDA OR DEDICATED INSTRUMENT

## Slide 36: THE RADIO

## Slide 37: RADIO USAGE
USUALLY BETTER OFF THAN ON
THIS CAMP AN EXCEPTION
100 MILE RANGE
RIDGE FLYING
DRAINS YOUR BATTERY AS IT DRAINS THE PATIENCE OF FELLOW PILOTS
RADIO MASA/RADIO WURTSBORO SQUEEZE

## Slide 38: SEAT-OF-THE-PANTS

## Slide 39: SEAT-OF THE PANTS
THERMAL ENTRY
VARIO FILTER

## Slide 40: THE VARIOS

## Slide 41: TYPES
ELECTRONIC
MECHANICAL
FLOW SENSING
PRESSURE SENSING

## Slide 42: EXTRAORDINARY SENSITIVITY

## Slide 43: T.E. MAGIC
GLIDER ENERGY IS MV2/2 + MGH (K.E + P.E.)
MGH IS = CONSTANT x STATIC PRESSURE
MV2/2 = CONSTANT x DYNAMIC PRESSURE
THE TOTAL ENERGY SOURCE IS STATIC + DYNAMIC!

## Slide 44: THE PRICE WE PAY
GUST SENSITIVITY
GUSTS ARE SCALE INVARIANT
“HILLS PEEP OVER HILLS, AND ALPS ON ALPS ARISE”
SLOW RESPONSE

## Slide 45: THE VOLTMETER

## Slide 46: MONITOR BATTERY CONDITION
% CAPACITY REMAINING
OVERALL HEALTH
EARLY IN-FLIGHT WARNING

## Slide 47: OPEN CIRCUIT V VS REMAINING CHARGE

## Slide 48: THE YAW STRING

## Slide 49: INSTALLATION
IDEALLY ON CG
OUT OF THE WAY
ATTACHING

## Slide 50: USE
STRAIGHT FLIGHT
CIRCLING FLIGHT

## Slide 51: SLIPPING AND SKIDDING

## Slide 52: GENERAL CONSIDERATIONS
12 (!) INSTRUMENTS IN MY PANEL, ONE ON THE CANOPY
NEED TO UNDERSTAND WHAT THEY ARE TELLING US
NEED TO KEEP EYES OUTSIDE OF COCKPIT
NEED BATTERIES THAT WORK WITH FUSES AT THE BATTERY
NEED AT LEAST ONE BACKUP BATTERY
NEED TO MONITOR BATTERY STATUS
NEED A SIMPLE AND CLEAR WAY TO SELECT BATTERIES
NEED TO DEVELOP A SCAN

## Slide 53: PRACTICAL CONSIDERATIONS
WIRES
  22 AWG IS ~0.02 OHMS/FT
TUBING
  VINYL TAKES A SET AND HARDENS, SILICONE BEST
FUSES
  BATTERYNSOURCE IMPEDANCE A FEW MILLIOHMS - MUST HAVE ONE ON EVERY BATTERY!
ANTENNAS
  GPS, ELT, COM
PROBES
  T.E.

## Slide 54: CAPACITIES
INSULATE
LOCATION AND TUBING LENGTH
ADIABATIC COOLING AND HEATING
SIZE
YOU CAN SHARE A T.E SOURCE, BUT NOT A CAPACITY

## Slide 55: MORE PRACTICAL CONSIDERATIONS
FILTERS
NEATNESS
BATTERY SELECT SWITCH

## Slide 56: ADJUSTING SUCTION
ADD LENGTH FOR MORE SUCTION