## Slide 1: Climbing
US Team/Region 1 Comps Doug Jacobs

## Slide 2
Why cover such basic stuff?
    Every XC flight is a race
distance vs. daylight
    Need to achieve reasonable speeds – 50mph +
to complete longer distances
    Most critical element in achieving XC speed is
climb rate achieved
    So lets review the basics on how to climb as fast as possible
Notes: Teaching Point
The best thing you can do to improve XC and racing speed is to climb better

## Slide 3
What does a thermal look like?
Discrete Bubbles
Constant Flow
Strength Variation -Strong in middle
-Weaker at edges
-Sink surrounding
-Narrow at the base
-Broader at altitude
-Churning internally
Notes: Teaching Point
Various thermal models are similar
Small lower, bigger higher
Stronger middle, weaker or sink outside
Churning
Not the same strength at all altitudes
Weak/narrow lower
Strongest in middle
Can fizzle out before cloudbase

## Slide 4: SO THAT’S WHAT A THERMAL LOOKS LIKE!
Notes: <number>
<footer>
<header>
Conical in shape, note the regions of reverse flow at various points on the cone surface – depending on the height at which you encounter this thermal there will indeed be a significant downdraft on entry, but not at all heights or from all directions. The thermal does indeed get bigger as it rises, and its quite clearly not homogeneous.

## Slide 5
Thermals are cyclical
Thermal changes dramatically over it’s cycle
Note the need for a triggering point – good to know when searching low
Notes: Teaching point
Must recognize life cycle of thermals
Must distinguish by cloud appearance
Look for trigger points low

## Slide 6
So how wide is a thermal?
200 Feet?
500 Feet?
1000 Feet?
2000 Feet
5000 Feet
All of the above?
Let’s mentally measure one
Glider going 60 kts travels approximately 100 ft/s
Let’s fly through some lift going 60 kts.
Notes: Teaching point
Most don’t know how small a thermal is
Instructor pretends he’s a vario
Goes “beep, beep, beep” like an audio in lift for 10 seconds, which is a long time, class starts to laugh
Lesson? – see, thermals aren’t that big – they’re little

## Slide 7
So, thermals are LITTLE! - Especially in the East
Just a few hundred feet across
How big is the circle you fly?
In a modern glass ship, at normal thermalling speed:
20 degrees of bank = 1000 foot circles
30 degrees = 600 foot circles
45 degrees = 500 foot circles
practical minimum = 450 foot circles
Hawks, eagles, and 1-26’s do much better
Here’s a web site with a radius calculator:
http://www.soarcsa.org/thinking_pages/soaring/turn_radius/turn_rad_knots.htm
Notes: Teaching point
So, to stay in, must make circle little to match
Bank angle critical in doing so

## Slide 8
Turn Radius Versus Bank Angles
Notes: Teaching point
Busy chart, but key insights
Notice how much bigger circle is between 20 and 30 degrees of bank – 50% or so
But not so much bigger between 30 and 40 degrees
Notice how much bigger circle is between 50 and 60 knots (on the 30 degree curve, worse on the 20 degree curve)
But no so much bigger on the 40 or 50 degree bank curve
Lesson – bank angle and speed critical to staying in thermal
Small bank and speed angle changes (perhaps unnoticed by pilot) make big difference in whether you stay in the thermal or not
Less experience pilots don’t recognize this, let bank angle and speed vary too much

## Slide 9
So – things to remember:
  Small Bank Angle Variations change the size of the circle a lot
  Small Speed Variations change the size of the circle a lot
  At small bank angles, small bank changes move the circle a lot
  At high bank angles, must make more noticeable bank changes
      to move the circle much
Why the heck is this important?
  New XC pilots tend to fly too flat a bank
  And let their bank angle wander
  And let their speed wander
While Thermalling, Fly:
Constant Speed
Controlled Banks
Notes: Read the slide

## Slide 10: TURNING TOO SOON
Notes: <number>
<footer>
<header>
A common mistake, driven by anxiety when low, and perhaps an element of wishful thinking, make it easy to start the turn too soon. Turning too soon guarantees both that you get to fly in sink and that you will spend additional time centering. In the case pictured here the vario climb indication would have still been increasing when the turn was initiated – a sure sign of turning too soon.

## Slide 11: TOO LATE
Notes: <number>
<footer>
<header>
It’s actually easier to turn too late than this picture suggests since you may well encounter the thermal further to one side or the other but regardless of the actual trajectory, the time to turn is either on a good surge or immediately after the vario reaches its maximum.

## Slide 12: JUST RIGHT
Notes: <number>
<footer>
<header>
Enjoy it when it happens which won’t be more than about 1/3 of the time even if you are good.

## Slide 13: WHICH WAY TO TURN?
A
B
C
Notes: <number>
<footer>
<header>
The further the entry course line is from a diameter, the greater the cost of a wrong way turn. There is little to be done about this however since we cannot know on approaching a thermal where the center is.
A) No need to worry - both ways are wrong, and there is no way to distinguish.
B) Right turn is favored, but unless the right wing lifts prior to the turn, the pilot does not know this.
C) The sufficiently lucky or sufficiently skillful pilot can perfectly time the turn, get the direction right, and be centered almost immediately.

## Slide 14: DAMN – TURNED THE WRONG WAY
A THERMAL MAY BE APPROACHED RADIALLY OR TANGENTIALLY
A RADIAL APPROACH GUARANTEES A WRONG DIRECTION TURN
A TANGENTIAL APPROACH HAS A 50% CHANCE
THE PROBABILITY OF TURNING CORRECTLY IS 1 IN 3
Notes: <number>
<footer>
<header>
The chance of turning the wrong way when entering a thermal on a chord is 50%. Add to this the certainty of turning the wrong way when entering on a diameter, and it is clear that in the absence of any additional clues, it’s likely that the turn into the thermal will be in the wrong direction. It helps to know that geometry and probability, not caprice, account for this.

## Slide 15
Thermal Centering Techniques
Best/Worst Heading Method
Flatten bank angle momentarily 270 degrees from best heading
Or
Straighten out 90 degrees after worst heading
Problems:
Vario Lags – what’s the best/worst heading really?
Gust Effects – can’t tell gusts from true lift
Flying straight is high risk – can fly out of thermal quickly
Notes: There are various centering techniques
None perfect
Thermals vary too much
Here’s a pretty mechanical approach
But has problems
Tie in the “flying straight” portion to what we just learned about thermal size – easy to lose the whole thing while flying straight, if you must, do it for only a very short period of time

## Slide 16
Bank Angle Change Methods
- Tighter in Lift/Open in Sink
When you don’t know where the core is
- Open in Lift/Tighter in Sink
When you know where the core is
Primary Problem for lower time pilots is flying past the lift, racking up in sink
Notes: Most experienced pilots do a mixture of this one
When encountering lift
rack into a turn
When hitting the sink
fly away from the sink
Requires constant hypotheses about where the core is

## Slide 17: TIMING THE TURN
VARIO
FEEL
VISUAL CLUES
Notes: <number>
<footer>
<header>
This is a critical skill and one hard to teach. It’s preferable to turn late rather than early since you have more information available. Botched thermal entries add up. The amount of time you can afford to invest in deciding whether or not to circle is inversely proportional to your height above the ground.
The vario is generally your best guide. Seat-of-the-pants can help but it’s hard to tell gusts from the real thing. Visual clues – birds, other glider, debris and of course cu are the most helpful.

## Slide 18: CENTERING
INITIAL CIRCLE
WORST VARIO HEADING
TRUE WORST HEADING
ROLLOUT HEADING
NEW CIRCLE
LANDMARK
Notes: <number>
<footer>
<header>
Glider established in climb but not centered
This is where you want to be
This is obviously the roll out heading for the correction but the vario won’t tell you this
If the vario had no lag it WOULD tell you the heading at right angles to the correction heading
If you knew the vario lag not in seconds, but in degrees it would still tell you – the lag is typically 45 degrees
45 degrees following the worst vario indication find a landmark on the bisector of the pitch and roll axes of the glider
When that landmark is on the nose roll out for two seconds, roll back in.
Repeat as needed.
It is helpful to translate seconds of vario lag to a fraction of a typical circle. For the sake of the discussion, I will assume that the circle takes about 16 seconds (45 bank). I will further assume that the vario lag is 2 seconds. This is 1/8 of a circle. The vario lag may be estimated well enough by trial and error.
Assuming that the glider is established in a circle but not yet centered, the correction is simple: 1/8 of the circle after the indicated point of worst lift, roll out for 1 second, then immediately re-establish the original bank.
It is easy to establish the heading on which to roll out: Just find a feature on the ground more-or-less aligned with the bisector of the wing and the fuselage axis, and roll out when the glider is heading to that feature.

## Slide 19: GUSTS AND THE TE VARIO
GUSTS CHANGE THE K.E. OF THE GLIDER
THE TE VARIO MEASURES ENERGY
TE VARIOS ARE GUST SENSITIVE!
Notes: <number>
<footer>
<header>
Everything good comes with a price tag attached. The price we pay for T.E. compensation is gust sensitivity. It is easy to see why this must be so: Any gust which contains a component aligned with the relative wind (which is to say ALL gusts other than those which are either vertical or at right angles to the relative wind) will change suction on the T.E. probe. A gust which with a component on the nose of the glider will increase suction and cause a positive deflection on the vario. The converse is true for a gust with a component on the tail of the glider. Neither effect is small, and both make it much harder to interpret the vario reading.
I will have more to say about gusts and the TE vario in my talk on instruments but for now will note that the “noise” of a gust is in fact signal, and that the TE variometer is doing exactly what is was designed to do – faithfully determining the total energy of the glider which does indeed increase when it encounters a (positive) gust. To make matters worse the sensation (“kinesthetics” is the vogue word) of flying into a positive horizontal gust is indistinguishable from the sensation of flying into a vertical gust, or a thermal.

## Slide 20
Things to dwell on while you thermal:
  Get to the center quickly and stay there
    Refuse to fly through the same sink twice
Be prepared to adjust the circle continuously
Choose speed/bank angle yourself – don’t let the thermal do it for you - Attitude constant
Look out the window for clues:
Above – emerging wisps, new cells
Level – birds, gliders, debris
Below – birds, gliders, dust devils, swirl patterns on leaves
Stay off the radio
This is hard enough as it is, and we haven’t even got to the decision making on where to go next
Notes: Go through the slide
Particular emphasis on speed/bank angle
LOOK UP – amazing number of pilots do not look where it would be most advantageous to look in a thermal – straight up – that’s where cloud and wisp development will tell you a lot
Thermalling is hard work – don’t distract yourself with radio calls, map reading, pee bags and the like
Justin Wills quote “If you can make a radio call and thermal at the same time, you haven’t optimized the thermal

## Slide 21
Thermalling Low:
Low saves are a fact of soaring
Routine in ridge flying
Very difficult much below 1000 feet – and that’s for experts
Typically very narrow with sharp boundaries between sink and lift
Typically very turbulent
And dangerous as hell with any wind speed
So:
- Have a field picked
- Add a bit more speed
- Expect to be in and out of sink
- Look for overall average positive climb
- Stay with what you got – it’ll probably get better
- Small circle adjustments
Notes: Getting low is a fact of life
Prepare for it
Stay calm
Stay with lift and wait for it to grow

## Slide 22
Practice (as usual) makes perfect (or at least safer)
Routinely practice the following at the end of the day with any excess altitude (well above pattern, of course, and after clearing turns)
15 Second Circles
65 knots
55 degree bank
Enter/Exit/Change Direction
Rigid Adherence to constant speed/bank angle
Yaw string in the middle – no “speed brakes”
Note constantly change required in rudder position for bank angle
Most pilots under rudder when they increase bank and over rudder when they reduce bank.
Get to Know your Airplane
  It’s easy to spin from a tight turn
  Sharp Turn
  Lots of rudder, left in place
  Opposite aileron to hold the bank constant, nose starts to fall
  Elevator to pull the nose up
  Look out below!
Notes: Must have full command of the glider and practice makes perfect
Most glass gliders WILL spin, contrary to popular notions. Try this in yours – well away from everyone – you’ll be surprised. But then you’ll recognize and be able to avoid

## Slide 23
Thermal Entry/Exit
Enter from the side, don’t aim for the middle
Vary your bank to fit yourself in
Turn in the same direction of the first sailplane in
Avoid just above or just below positions
Avoid cutting across the nose of a slow climber
Don’t bomb through the center upon leaving, no matter what XX says
Notes: Go through the slide

## Slide 24
Finding Thermals
Lift is where you find it . . . .
But you can improve your chances quite a bit
Cloud/cloud shapes
Wind direction, effect
Cloud cycle
How far to that cloud?
How long until it fizzles
Markers - use your eyes!
Gliders
Birds
Dust/smoke
Ground surfaces
Sun/ground angles
Trigger points
Ridge tops
Vegetation changes
Lake borders
Develop a mental profile of the day
Develop a feel for lift on your wings
And don’t do this
Notes: Thermal search
Become a student of clouds
Know cloud cycle from the ground before you take off, from climbing before you start your task, get mental image of start-middle-end of cloud development
LOOK – pilots I ride with just don’t see as much as I think they should – lots of clues are missed
Fly the heading you want to fly, fly straight lines, else the lift will push you around through sink

## Slide 25
Practical Observations . . .
From Thermals I’ve known
Strong lift goes high
But interthermal distances are large
so don’t get low
Weak lift goes only to moderate altitudes
But tends to be more generously distributed
Thermal strength varies quite a bit
One out of five are best
Avoid the weak ones except in need
There’s an optimal XC height band
Top 2/3rd’s of the convection band is workable
Top 1/3rd is the fastest
Notes: Read slide