## Slide 1: CRUISING FOR SPEED
TECHNIQUES FOR EFFICIENT INTERTHERMAL SOARING

## Slide 2: INTRODUCTION
CRUISING = 60%-80% OF FLIGHT
MACREADY STILL RULES – BUT --
Notes: SeeYou L/D
DB’s flight

## Slide 3: PROGRAM PLAN
REVIEW CLASSIC MACREADY THEORY
WIL SCHUEMANN’S PAPER
  The Price You Pay For Macready Speeds
JOHN COCHRANE’S PAPER
  Just A Little Faster Please
TECHNIQUES FOR SPECIFIC SITUATIONS
Notes: The implications of these papers in our evolving use of MacCready theory

## Slide 4: Classic Macready Theory
History
Assumptions
  Lift constant for altitude
  All thermals same strength
  Next thermal strength known
Notes: 1938 Polish pilots began “best speeds’ curves—lost in war
1948 Karl Nickel published tangential construct
1948 Macready published speed ring design

## Slide 5: Classic Macready Theory (cont.)
Calculate optimal inter-thermal speed for maximum x/c ave. speed

## Slide 6
Effect of inter-thermal sink– essentially subtracts from achieved climb rate
Effect of Headwind/Tailwind--none except on final glide
Water ballast-- shifts polar down to right

## Slide 10: PINCIPLE OF OPTIMIZATION

## Slide 11: PROBLEMS WITH MACREADY
do not know next climb rate
Climb rate varies with altitude
Don’t know sink between thermals– varies constantly

## Slide 12
Wil Schuemann- renaissance soaring man
  Total energy compensation box
  Water ballast
  Winglets
  Discus plan-form
  Seminal paper on modified MacCready flight
    Soaring symposia—1972– see references
Notes: The ASW-12 experimental platform

## Slide 13: The Price You Pay For Macready Speeds by Wil Schuemann

## Slide 14
Cruise speed vs. Ave. x/c speed
  minimal difference +/- 8-10 knots
  Big difference at best L/D
Effect on range – does slower speed increase range? Yes with respect to airmass- more range, larger chance to find special thermal

## Slide 15
Notes: Shows curves for different inter-thermal rising or sinking air rates for standard class glider
Rise shifts L, sink shifts R,
But curves suggest much latitude

## Slide 16: Practical problems with Macready
What is the next thermal strength??
Chasing the needle– may do more damage than good
Distracts from other tasks

## Slide 17: Lessons learned
Speed variations 8-10 knots from ideal Macready minimal impact on ave. x/c speed
Speeding in sink gains little
Range gained with slowing
But perfect speed adherence would give slightly higher speeds.

## Slide 18
Schuemann’s conclusions
  A moderate speed with little variation costs very little speed
  Reducing MacCready intensity yields more time to think!!! And look outside
  Increasing range may improve thermal selection
  Slower flight makes air easier to assess

## Slide 19: John Cochrane
  PHD economics, U. of Chicago dept. Finance
  Highly successful competition pilot
  Regular contributor to Soaring magazine

## Slide 20: Just A Little Faster Please John Cochrane
Speed and modern MacCready theory-observations
  MacCready still key to in-flight speed decisions
  MacCready determines cruise speed--- the mathematical solution is still valid
  But what is the correct MacCready value?
    Reichmann’s elliptical thermal lift concept- bottom and top are usually less than mid-level climb rate
    Likelihood of finding best thermals goes down with altitude

## Slide 21
Random lift distribution curve plotted against altitude
  Assumes thermals vary in strength quite a bit
  There are many weak thermals to use to save a flight low
  There are a few really good thermals

## Slide 22: Proper MacCready setting drifts down as glider gets lower

## Slide 23
Thermals are variable
Steadily reduce MacCready as altitude lower
Leave weak thermals to search as get higher
Average MacCready much lower than best seen
Always adjust MacCready to expected future—save altitude now!!!

## Slide 24: John Cochrane (cont.)
CENTERING TIME-AT THERMAL ENTRY
  Often several circles
  Dilutes average rate of climb
  Makes stopping for short climbs less efficient
  Longer down low and on windy days
  Effect larger for strong thermals
  Supports trying to pick easily centered thermals

## Slide 25: Cruising techniques
Cruising with cumulus clouds
  Streets
    Speed to fly– MacCready still applies
    Altitude-- higher better but need to see
    Deviation angles up to 30 degrees, occ. more
    Bridging to next street
    Often best speed will cause falling away from clouds
    “End of street” planning
      Get high

## Slide 26: Crossing big blue holes and flying blue days
Assess– why blue??
Get high and try to stay high
Slow until time for assessment –may be good but dry– or not!!!
Look for gliders- good thermal markers

## Slide 27: Weak blue day strategy
Greater uncertainty warrants more conservative MacCready
Find some company 3-5 gliders not 20
Spread out when cruising with other gliders—don’t hide behind
Lift asymmetries and lift lines –lead to thermal
Read the ground

## Slide 28: Water ballast
Adjustable wing-loading
Alters climb and cruise
  Slows climb and increases circle radius and speed
  Enhances cruise performance-progressively at higher cruise speeds
  Rule of thumb– water helps above 350 ft/min ave climb

## Slide 29: Water ballast (cont.)
  Especially helpful in streeting situations where cruise extended
  Most competition pilots load up
  Don’t dump too soon– day may get better
  Don’t keep it too long
  Sometime dump a little—eg. Low saves (small thermal)

## Slide 30: Cumulus clouds
Cloud types
  Cumulus humilis
  Cumulus congestus
  Cumulo-nimbus

## Slide 31: Cumulus humilis

## Slide 32: Isolated or random cumulus clouds read tops as well as bottoms

## Slide 33: Cumulus congestus

## Slide 34: Cu-nim

## Slide 35: Thermal assessment
Entry burble with + or – sink
  Consider slowing to improve reaction time and feel
  Beware premature turn– use the glider as a probe
  be patient
  Carefully sense for asymmetry
  Expect to go outside the thermal on first turn

## Slide 36
Entering thermals under cu
  Mental picture of top---- plan ahead
  Bridging wisps
  Speed– when to slow
  Feel your way in while trend toward visual clues

## Slide 37
  Darkest areas
  Look at upwind side of cloud
  Sunny side ???
  Where was the last lift located
Be discriminating--- have an idea what you expect

## Slide 38
  Cloud departure
  plan ahead
  speed choices
  use the rest of the cloud
  look for bridges to next path
  Ideally should have idea where next stop will be

## Slide 39: Blue thermal cruising
Wind direction key!!!
  Wind arrow on Ilec or GNII, etc
  Streets almost always on the wind
  Feel for the lines of lift and do this continuously
  Deviate onto the lines of lift (energy paths)

## Slide 40: Blue thermal cruising (cont.)
  ? Slower– greater range when weak and blue
  Practice centering lines of lift on blue days
    Feel for asymmetric lift, and make small turns into it
    Try to sustain reduced sink – can augment achieved L/D substantially, extend range, lead to a thermal

## Slide 41: When to stop in general
Long cruise legs reduce centering loss
Set a height band floor—usually ~ top 30- 40% of thermal–
Below 50% begins to disconnect from clouds
But depends on thermal strength profile for the day- height band

## Slide 42: Classic Turnpoint strategy
Up-wind low, downwind high conundrum
  Great theory but loaded with traps
  Turn-points are always in sink or blue holes
  Use the whole circle if needed for good timing management
  Watch out for traffic
  Bottom line-plan ahead!!!!!

## Slide 43: When to slow up (changing gears)
Cochrane’s theory– progressive
When going from cu to blue
Cirrus overcast ahead
Known or visible wet area ahead—lake, known shower history, standing water,
Multiple low gliders ahead
Lots of whining on the radio

## Slide 44: Low saves
Go slow for max range
Look for birds, other gliders, dust devils
ridges, rock piles, fire, smoke, edge of lake or woods
Take anything and work its edges, especially up-wind-- be patient
Quit at a safe altitude– know your limits

## Slide 45: Water ballast
Adjustable wing-loading
  Slows climb directly, increased circle speed and diameter (farther away from core)
  Improves glide performance-greater range, ave. speed
  Rule of thumb-keep water if ave. lift 350 ft./min or more
  Especially helpful on long streets, ridges

## Slide 46: Water ballast use (cont.)
Don’t dump too soon
May need to dump a portion
  Low saves
  Thermals generally small in diameter
  Don’t dump in gaggle thermals

## Slide 47: Water ballast (cont.)
Check your system
Practice before you go to a contest
  Loading’s a hassle
  Flies differently
  Adds an interesting element of complexity

## Slide 48: Psychology
        Complex multi-tasking exercise
        Effect of stress on efficiency
        x/s stress management, avoidance and recovery

## Slide 49: What we really do
Conservative MacCready dictates ave. Speed
Plan ahead, WAY AHEAD
Not a lot of zooming—gentle speed changes
Slower with lower highly variable
Major emphasis on best track (thus improved L/D)
Extreme emphasis on finding best thermals
Leave mediocre thermals as soon as safe

## Slide 50: What we do (cont.)
Major deviations are the norm
Do what it takes to avoid out-landings
Remember the sky usually is not falling
Have fun, don’t obsess about falling behind
Everybody has a bad day sometime
Practice, practice, practice
Fly for speed every time you fly
Get better!!!

## Slide 51: Recommended reading
Cross-Country Soaring: Helmut Reichmann
Introduction To Cross-Country Soaring: Kai Gertson http://www.flsc.org/XCountry/Cross-CountryB0202.pdf
The Price You Pay For MacCready Speeds: Wil Schuemann http://www.betsybyars.com/guy/soaring_symposia/

## Slide 52
Just A Little Faster Please: john Cochrane http://faculty.chicagogsb.edu/john.cochrane/research/Papers/#maccready

## Slide 53: Let’s fly
The end