## Slide 1: Climbing
US Team/Perry XC/Racing Camp
Doug Jacobs

## Slide 2
Why cover such basic stuff?
  Reasonable Goals for Course Participants:
Silver/Gold/Diamond Badges
Governor’s Cup Distances
Little Guys Meet
GTA Racing
State Records
    Every XC flight is a race
distance vs. daylight
    Need to achieve reasonable speeds – 50mph +
to complete longer distances
    Most critical element in achieving XC speed is
climb rate achieved
    So lets review the basics on how to climb as fast as possible
Notes: Teaching Point
The best thing you can do to improve XC and racing speed is to climb better

## Slide 3
What does a thermal look like?
Discrete Bubbles
Constant Flow
Strength Variation -Strong in middle
-Weaker at edges
-Sink surrounding
-Narrow at the base
-Broader at altitude
-Churning internally
Notes: Teaching Point
Various thermal models are similar
Small lower, bigger higher
Stronger middle, weaker or sink outside
Churning
Not the same strength at all altitudes
Weak/narrow lower
Strongest in middle
Can fizzle out before cloudbase

## Slide 4
Thermals are cyclical
Thermal changes dramatically over it’s cycle
Note the need for a triggering point – good to know when searching low
Notes: Teaching point
Must recognize life cycle of thermals
Must distinguish by cloud appearance
Look for trigger points low

## Slide 5
So how wide is a thermal?
200 Feet?
500 Feet?
1000 Feet?
2000 Feet
5000 Feet
All of the above?
Let’s mentally measure one
Glider going 60 kts travels approximately 100 ft/s
Let’s fly through some lift going 60 kts.
Notes: Teaching point
Most don’t know how small a thermal is
Instructor pretends he’s a vario
Goes “beep, beep, beep” like an audio in lift for 10 seconds, which is a long time, class starts to laugh
Lesson? – see, thermals aren’t that big – they’re little

## Slide 6
So, thermals are LITTLE! - Especially in the East
Just a few hundred feet across
How big is the circle you fly?
In a modern glass ship, at normal thermalling speed:
20 degrees of bank = 1000 foot circles
30 degrees = 600 foot circles
45 degrees = 500 foot circles
practical minimum = 450 foot circles
Hawks, eagles, and 1-26’s do much better
Here’s a web site with a radius calculator:
http://www.soarcsa.org/thinking_pages/soaring/turn_radius/turn_rad_knots.htm
Notes: Teaching point
So, to stay in, must make circle little to match
Bank angle critical in doing so

## Slide 7
Turn Radius Versus Bank Angles
Notes: Teaching point
Busy chart, but key insights
Notice how much bigger circle is between 20 and 30 degrees of bank – 50% or so
But not so much bigger between 30 and 40 degrees
Notice how much bigger circle is between 50 and 60 knots (on the 30 degree curve, worse on the 20 degree curve)
But no so much bigger on the 40 or 50 degree bank curve
Lesson – bank angle and speed critical to staying in thermal
Small bank and speed angle changes (perhaps unnoticed by pilot) make big difference in whether you stay in the thermal or not
Less experience pilots don’t recognize this, let bank angle and speed vary too much

## Slide 8
So – things to remember:
  Small Bank Angle Variations change the size of the circle a lot
  Small Speed Variations change the size of the circle a lot
  At small bank angles, small bank changes move the circle a lot
  At high bank angles, must make more noticeable bank changes
      to move the circle much
Why the heck is this important?
  New XC pilots tend to fly too flat a bank
  And let their bank angle wander
  And let their speed wander
  But not Perry Camp Graduates!!!
While Thermalling, Fly:
Constant Speed
Controlled Banks
Notes: Read the slide

## Slide 9
Thermal Centering Techniques
Best/Worst Heading Method
Flatten bank angle momentarily 270 degrees from best heading
Or
Straighten out 90 degrees after worst heading
Problems:
Vario Lags – what’s the best/worst heading really?
Gust Effects – can’t tell gusts from true lift
Flying straight is high risk – can fly out of thermal quickly
Notes: There are various centering techniques
None perfect
Thermals vary too much
Here’s a pretty mechanical approach
But has problems
Tie in the “flying straight” portion to what we just learned about thermal size – easy to lose the whole thing while flying straight, if you must, do it for only a very short period of time

## Slide 10
Bank Angle Change Methods
- Tighter in Lift/Open in Sink
When you don’t know where the core is
- Open in Lift/Tighter in Sink
When you know where the core is
Primary Problem for lower time pilots is flying past the lift, racking up in sink
Notes: Most experienced pilots do a mixture of this one
When encountering lift
rack into a turn
When hitting the sink
fly away from the sink
Requires constant hypotheses about where the core is

## Slide 11
Things to dwell on while you thermal:
  Get to the center quickly and stay there
    Refuse to fly through the same sink twice
Be prepared to adjust the circle continuously
Choose speed/bank angle yourself – don’t let the thermal do it for you - Attitude constant
Look out the window for clues:
Above – emerging wisps, new cells
Level – birds, gliders, debris
Below – birds, gliders, dust devils, swirl patterns on leaves
Stay off the radio
This is hard enough as it is, and we haven’t even got to the decision making on where to go next
Notes: Go through the slide
Particular emphasis on speed/bank angle
LOOK UP – amazing number of pilots do not look where it would be most advantageous to look in a thermal – straight up – that’s where cloud and wisp development will tell you a lot
Thermalling is hard work – don’t distract yourself with radio calls, map reading, pee bags and the like
Justin Wills quote “If you can make a radio call and thermal at the same time, you haven’t optimized the thermal

## Slide 12
Thermalling Low:
Low saves are a fact of soaring
Routine in ridge flying
Very difficult much below 1000 feet – and that’s for experts
Typically very narrow with sharp boundaries between sink and lift
Typically very turbulent
And dangerous as hell with any wind speed
So:
- Have a field picked
- Add a bit more speed
- Expect to be in and out of sink
- Look for overall average positive climb
- Stay with what you got – it’ll probably get better
- Small circle adjustments
Notes: Getting low is a fact of life
Prepare for it
Stay calm
Stay with lift and wait for it to grow

## Slide 13
Practice (as usual) makes perfect (or at least safer)
Routinely practice the following at the end of the day with any excess altitude (well above pattern, of course, and after clearing turns)
15 Second Circles
65 knots
55 degree bank
Enter/Exit/Change Direction
Rigid Adherence to constant speed/bank angle
Yaw string in the middle – no “speed brakes”
Note constantly change required in rudder position for bank angle
Most pilots under rudder when they increase bank and over rudder when they reduce bank.
Get to Know your Airplane
  It’s easy to spin from a tight turn
  Sharp Turn
  Lots of rudder, left in place
  Opposite aileron to hold the bank constant, nose starts to fall
  Elevator to pull the nose up
  Look out below!
Notes: Must have full command of the glider and practice makes perfect
Most glass gliders WILL spin, contrary to popular notions. Try this in yours – well away from everyone – you’ll be surprised. But then you’ll recognize and be able to avoid

## Slide 14
Thermal Entry/Exit
Enter from the side, don’t aim for the middle
Vary your bank to fit yourself in
Turn in the same direction of the first sailplane in
Avoid just above or just below positions
Avoid cutting across the nose of a slow climber
Don’t bomb through the center upon leaving, no matter what XX says
Notes: Go through the slide

## Slide 15
Finding Thermals
Lift is where you find it . . . .
But you can improve your chances quite a bit
Cloud/cloud shapes
Wind direction, effect
Cloud cycle
How far to that cloud?
How long until it fizzles
Markers - use your eyes!
Gliders
Birds
Dust/smoke
Ground surfaces
Sun/ground angles
Trigger points
Ridge tops
Vegetation changes
Lake borders
Develop a mental profile of the day
Develop a feel for lift on your wings
And don’t do this
Notes: Thermal search
Become a student of clouds
Know cloud cycle from the ground before you take off, from climbing before you start your task, get mental image of start-middle-end of cloud development
LOOK – pilots I ride with just don’t see as much as I think they should – lots of clues are missed
Fly the heading you want to fly, fly straight lines, else the lift will push you around through sink

## Slide 16
Practical Observations . . .
From Thermals I’ve known
Strong lift goes high
But interthermal distances are large
so don’t get low
Weak lift goes only to moderate altitudes
But tends to be more generously distributed
Thermal strength varies quite a bit
One out of five are best
Avoid the weak ones except in need
There’s an optimal XC height band
Top 2/3rd’s of the convection band is workable
Top 1/3rd is the fastest
Notes: Read slide