## Slide 1: Cross-country Soaring
Promote cross-country flying
Propose the FLSC Cross-country Program
Safety and cross-country flight
2004 FLSC Safety Seminar Doug Cline

## Slide 2: Proposed FLSC Cross-country Program
Promote and teach cross-country flight
Enhance flying skills
Engender more enthusiasm, enjoyment, and camaraderie in FLSC
Stimulate membership growth
Encourage member participation in national contests
Build on successful mentoring programs introduced by Kai and John
Introduce a handicapped cross-country mileage annual award based on SSA Sports Class Handicaps
Goals:
Approach

## Slide 3: SSA Handicaps 2003
Sailplane Owner SSA Handicap
Jantar 2 Tom Roberts 0.865
304CZ-17 Chuck Zabinski 0.879
ASW27 Kai Gertsen 0.880
John Seymour 0.880
ASW20B Ted Falk 0.900
304CZ-15 Chuck Zabinski 0.950
304C Jari Wallach 0.950
Pegasus 101B Doug Cline 0.955
ASW19 Linda/Ann/Rick 0.970
Matt Lyon 0.970
Jim Rizzo 0.970
Grob 104 Speed Astir Glenn Noonan 0.975
SGS 1-35 Toni Meli 0.975
Bill Robinson 0.975
Libelle 201 Doug Bradley 1.013
SGS 1-34 Lee Bernardis 1.200
K6E Ed Seymour 1.260
Bergfalke 3 Tom Roberts 1.440
ASK21 FLSC 1.180
Russia AC 4A FLSC 1.193
Blanik L13 FLSC 1.460
SGS 1-26A FLSC 1.650
Notes: Tom has the highest and lowest performing private gliders. He is determined to win and is thus playing both ends of the handicap. He needs to fly the Jantar 1.66 times further than the Bergfalke.

## Slide 4: FLSC Annual Cross-country Award
Based on total handicapped cross-country mileage for season
Pilot selected task using authorized turn points
Minimum course length 30 handicapped statute miles
Minimum time on course must exceed one hour
No turn point can be claimed twice except when there are at least two intervening turn points
GPS recording not required but encouraged
Other Cross-country Awards
Tom’s proposed “Boxer Shorts Derby” for first glider to soar to Brokenstraw to reclaim the Boomerang Trophy.

## Slide 5: Region 3 Turn points

## Slide 6: Training and mentoring
Fly ASK-21 or Blanik L13 with experienced cross-country pilot
Follow the leader with one or more experienced mentors in individual solo ships
Fly recommended tasks alone
Replay and critique cross-country flights

## Slide 7: Benefits of Cross-country Program
Benefit to you
Enjoyment, excitement, and satisfaction
Enhance flying skill
Benefit to FLSC
Stimulate camaraderie and growth in membership
Develop a nucleus of cross-country and competition pilots.
[They comprise the core of the FLSC and the instructor pool, e.g. Harris Hill]

## Slide 8: Safety and cross-country flight
Preflight: Pilot health and safety
Hydration: Drinking water plus urine relief capability
Wellness: Fitness, rest, nourishment, lack of stress
Dress: Hat, sun block, lip balm
Recent flight experience

## Slide 9: Preflight: Equipment
Thorough preflight plus critical assembly check.
Parachute
Cell phone plus necessary telephone numbers
Audio total-energy variometer is essential
Radio
Battery fully charged
Mc Cready ring, flight computer, or list of the speeds to fly
Set altimeter to msl
GPS recorder, barograph, or camera ready and switched on.
Trailer plus retrieve vehicle ready to roll: car keys, lights, fuel.

## Slide 10: GPS Logger
Strongly recommend GPS :
Navigation
Emergency fields
Final glide
Turn point validation
Flight analysis

## Slide 11: Preflight: Weather and route planning
Weather briefings: Weather Channel, ADDS, soundings, FAA FSS, Blipmaps
Blipmaps: Determine predicted thermal strength, height of critical updraft strength, cloud base, winds, wind shear, potential for over development, thunderstorm [CAPE]
Select optimum route for predicted weather, plus topography, cloud streets, emergency landing areas/airports.
Blipmaps:
RUCS & ETA

## Slide 12: Preflight: Navigation
Prepare map, mark turn points
Draw concentric circles every 5sm for final glide estimation
Study turn-point details, map, prominent landmarks
Identify useful emergency airports.
List of required radio frequencies
Check for restricted airspace
Coordinate flight plans, radio frequencies, with other pilots

## Slide 13: Local flight: xc training
Get to know the performance characteristic of your sailplane
Practice final glides to DSV on every flight. Allow for a safe altitude cushion
Practice precision patterns and landings on every flight
Perform patterns without reference to altimeter
Complete flare for minimum touch down speed
Evaluate fields both when flying and driving
Study the bible: “Introduction to Cross-country Soaring” by Kai Gertsen

## Slide 14: XC flight technique: Where to go?
Identify signs of thermal streets, [clouds]
Establish relationship of optimum lift to clouds, sunny side, upwind?
Follow path of short cycling wisps
Stay upwind of course line
Follow cloud streets even if 30o off track [<15% longer distance]
On blue days use gentle zig-zag on course to find blue thermals
If long region of sink, turn 90o to avoid sink street. Do not make 180o

## Slide 15: XC flight technique: Where to go?
Watch conditions while circling and plan ahead. Use cloud shadows to estimate distance to clouds. Glide ratio roughly 5nm/1000’
Identify prime areas of lift, baked bare ground, high ground, sun orientation, ridges
Avoid areas likely to have sink, e.g. downwind of lakes or irrigated areas.
Watch for soaring birds, sailplanes, fires.
Keep track of wind from thermal drift, smoke
Constantly monitor and stay within range of landable terrain

## Slide 16: How fast to fly?
Primary object is to get to the top of the next thermal as fast as possible. The same requirement applies to both competition flying and cross country flight.
Optimum inter-thermal speed depends on average rate of climb for the NEXT thermal plus the instantaneous sink rate of air. Use a McCready ring or computer.
McCready setting should be the average climb rate for the complete thermal; about half the perceived climb rate
Adjust McCready setting depending on height. Be conservative when low.
Constantly be alert to changing conditions and be prepared to change gear

## Slide 17: Mc Cready Speed-to-fly theory [“Cross-country Soaring” by Helmut Reichmann]

## Slide 18: Finding Thermals
When you’re high … fly the sky
Cu, wisps, haze domes
Birds, debris, gliders
When you’re low … look below
Terrain, junk yards, hay fields, heat source
Smoke, crop movement, flags, debris
Spacing is related to convection depth
Mark and return to excellent thermals

## Slide 19: When to thermal?
Minimize time circling to maximize speed
Decide on minimum rate of climb for that altitude based on the McCready setting
Acceptable climb rate depends on the altitude
Operating altitude band. Stay in the upper half of the convection layer until experienced.
For lift below minimum climb rate, use dolphin flight path slowing down in weak lift and vice versa
Maintain situational awareness, watch for soaring birds, sailplanes.

## Slide 20: Optimal thermalling
Must optimize rate of climb. The average speed nearly proportional to average achieved climb rate
Concentrate and strive for maximum climb rate
Continually scan for traffic
Thermalling time includes time to center thermal, therefore center quickly
Thermal at angle of bank 35o-55o at optimal speed for that wing loading.
Radius of curvature = v2/gtanθ. Thus minimum speed is desirable to fly in the stronger parts of the thermal core.

## Slide 21: Optimal thermalling conditions

## Slide 22: Optimal thermalling 2
At low altitude bank 35o immediately lift detected since thermal diameter is small
At high altitude can delay turn to explore larger diameter thermal profile
Direction of turn should be towards the rising wing
Make 270o correction if center of thermal missed

## Slide 23: Kai’s summary for thermalling
Always turn towards rising wing
When encountering a thermal low, do not hesitate to turn immediately
At high altitude do not turn until climb rate approaches expectations.
Immediately bank steeply to minimum 35o when entering thermal
If wrong direction straighten out momentarily after 270o
Do not change direction of turn
Shift aggressively if there is sink on one side of thermal. Do not go through sink twice
If lift all around shift in small increments. Continually keep optimizing.
Do not over-control, always use minimal smooth control movements
When lift increasing reduce bank to move circle in that direction
Tighten the turn on a surge and vice versa
Concentrate and never be satisfied
When low then steeper turns are needed and are safer
If low stay with what you have. Safe speed. Turn off the radio

## Slide 24: Off-airport landings
FLSC 2003: XC flight led to 3 airport plus 1 off-airport landing. Local flight led to two off-airport landings [1-26, L13]. 579 tows for season thus probability low.
Higher performing gliders usually can reach an airport. Low performance ships like the 1-26 and L13 can land on a dime which partially compensates for their poorer penetration.
Be careful since some private strips may not be mowed wide enough for a 15m wingspan glider

## Slide 25: Serious Hazards
Wires
Fences
Slopes

## Slide 26: Wires; the invisible foe
Wires usually are almost invisible from the air. Assume they exist in the following situations:
  Between two poles
  Between a pole and group of trees
  Between a road and a house
  Over or along a road
  Going into any building
  For high tension power lines beware of the thin ground wire that usually is placed above the visible thicker power cables.

## Slide 27: Wire Fences
Wooden fences easy to see and avoid.
Single strand electric fences with steel posts are literally invisible and are lethal. Can garrote the hapless pilot
Never land or roll across two different texture crops
A slightly different textured surface in one section of a field may indicate the presence of a fence, never cross such a boundary

## Slide 28: Slopes
Hard to detect the gradient of a slope from the air
In the Northeast the terrain on the hill typically is hilly while it is flatter and level in the valleys. [Naples area]
Landing in the valley gives you additional altitude available to find lift.
View the field from at angle of about 300 from the horizontal to maximize detection of the slope
Creeks and water are always at the lower elevation
Any slope detected from the air is steeper than you think, and too steep for a downhill landing
If there is any slope at all, you must land up-hill regardless of wind direction
Landing across a slope is not recommended, it is a tricky maneuver.
Beware of downdraft on the downwind side of hill top landing site

## Slide 29: Field selection
2000’AGL: Monitoring of landing areas becomes more critical
Fly towards generally landable areas
Identify hills that may create surface wind or turbulence problems
Avoid areas with visible slope
Note TV towers and power lines
If low turn off radio if not at an airport

## Slide 30: Field selection 7S checklist
1500’AGL: Select and commit to landing field based on the 7S criteria
Surface wind: Strength and direction
Size: Assess minimum length >1000’. Visual illusion makes a narrow field look longer etc
Shape: Select best direction to land. Select IP, downwind and base locations for standard pattern..
Slope: Up-hill landing needs 5-10kts more airspeed to perform pitch up. Expect strong sink on down wind side of a hill
Surface: Fences, furrows, and crops
Surroundings: Avoid obstructions to approach such as buildings, wires, trees. Reduce effective field length by 10x height of obstruction
Stock: Avoid fields with animals, [Especially if flying a PW5]

## Slide 31: Field selection
Are you really sure that field is long enough?

## Slide 32: Pre-landing check
700’ AGL; Landing checklist
Water [1.8 reduction factor in kinetic energy]
Wind [2 times reduction factor in KE between downwind and upwind landing for a 10kt wind]
Wires [Power lines, fences etc]
Wheel [Down and locked]
Speed [Adequate safe pattern speed, do not confuse with minimum energy landing speed]
Trim
Airbrakes cracked
Lookout
Landing area

## Slide 33: Pattern and landing
IP at 700.
Do not crowd downwind leg, leave enough room for an adequate base leg
Adequate pattern speed appropriate to wind conditions. NOT at minimum speed
Perform downwind to base turn to maintain continuous view of touch down point
Base and final leg should be long enough to make unhurried minor corrections
Maintain strict speed control on final
Use complete flare-out on every landing. If high crop, flare as if the top of the crop is the ground.
On touch down immediately apply maximum brake to minimize roll distance. [Rocks, gopher holes, etc]

## Slide 34: Post-landing procedures
Relax and congratulate yourself for superior airmanship
Secure the sailplane.
Use a cell phone to call for help
Contact the owner of the field. Be courteous, polite and thank owner. The FLSC must maintain good relations with the community; also this will be needed by the next pilot who lands in that field.

## Slide 35: Cross-country soaring
Come participate in the xc program this year
Relatively safe in our region
Exciting, exhilarating, challenging
Enhance your flying skill
Stimulate camaraderie and growth in membership
Develop a nucleus of xc and competition pilots.
Maximize our enjoyment of the soaring experience

## Slide 36: Acknowledgements
This presentation borrowed extensively from the excellent article “ Introduction to Cross-country Soaring” by Kai Gertsen and the Soaring Safety Foundation Master Instructor Cross-country Program Handbook.